## Slide 1: Keeping Your Firefighters From Killing Themselves!
John Norman
Retired Chief of Special Operations, FDNY
Notes: 1

## Slide 2: Hints for Class Participation
When asked to participate, do so.
  Take a stand on the question, right or wrong. No one will die here today as a result of your decisions.
Respect the opinions of others. They are taking a stand.
Have fun.
Don’t beat DEAD HORSES.
Help the instructor meet the goals of the class.

## Slide 3: Start feeding your “300 Year old mind.”

## Slide 4: We have learned a great deal about Firefighter deaths.
Notes: 4

## Slide 5: We have identified very few new phenomenon- for example, Extreme Wind Driven Fires
Notes: 5

## Slide 6: But most deaths are not the result of new hazards …
Notes: 6

## Slide 7: ….Instead, They Are the Result of the Same Causes That We Have Been Dying From for Decades.
Notes: 7

## Slide 8: Everyone Needs to Learn These Lessons, They’re Not Just a Big City Problem
60 Ff. Deaths In 2017
9 at Structure Fires*
*Source- NFPA
Notes: 8

## Slide 9: 9 Deaths Occurred While Responding or Returning
No Matter How Serious the Alarm is,
YOU DON’T DO ANY GOOD IF YOU DON’T GET THERE!!!
Notes: 9

## Slide 10: Structure fires have three factors that play a role in FF Safety
The Structure
  Older “legacy” buildings
  Newer lightweight
The Contents
The Firefighters

## Slide 11: The environment we are operating in HAS CHANGED dramatically in the last 48+ years

## Slide 12: Dramatically larger plastics fire load
The average home or apartment contains over 3,500 lbs of plastic.
Faster fire growth
More toxic fire gases

## Slide 13: Energy Efficient Windows
Hold heat and toxic gases in
Do not self vent until well into the fire
Require additional personnel and effort to thoroughly vent

## Slide 14: Tight Building Syndrome
Hold in heat and toxic gases
Hastens flashover
Creates more toxic environment
Increases possibility of backdraft

## Slide 15: The Impact 249 Deaths at Structure Fires 2000-2017*
99 Asphyxiation/Smoke
47 Burns
53 Heart Attack
49 Crushing/Trauma
Source: NFPA / USFA
*Excluding the 343 FF Deaths at the World Trade Center on 9/11/2001
Notes: 15

## Slide 16: Reasons for Firefighter Deaths- Lack of Understanding of Smoke Fire Behavior Flashover Backdraft
Notes: 16

## Slide 17: What is Smoke?
Smoke is Unburned Fuel Gases & Solids Including Carbon Monoxide (CO), Cyanides & Carbon (Soot)
Notes: 17

## Slide 18: Reasons for Firefighter Deaths
Asphyxiation and Smoke Inhalation were leading causes of death.
1970
Notes: 18

## Slide 19: Today-Universal SCBA Use
3 Asphyxiation/Inhalation Deaths in 2016 !
Notes: 19
19

## Slide 20: 0f the 99 Asphyxiation Deaths
36Caught by Structural Collapse
31 Caught by Fire Growth, Flashover, or Backdraft
23 Lost/Disoriented in Structure
9 Fell Through Holes in Floor
96 out of 99 Were Wearing SCBA!
  Two that weren’t were fighting fires in their own homes.
Notes: 20
20

## Slide 21: More Deadly Fire Gases
Since 1970 fires have tripled the BTU output, but…..
Smoke output can be as much as 20 times more toxic from synthetics
Energy Efficient Windows and insulation combine to trap all these gases inside with us
Notes: 21

## Slide 22: Burning polyurethane foam releases dangerous chemicals such as hydrogen cyanide, and dioxin

## Slide 23: Toxicity of today’s smoke is far worse than in the past. They incapacitate first, making escape impossible, before killing.

## Slide 24: Vent Thoroughly, Once Water On Fire Conditions Change, Masks Can Fail or You Can Be Entangled
Notes: 24

## Slide 25: When Evaluating Smoke, Look at:
Color
Volume
Movement
Location
Notes: 25

## Slide 26: Grey or Brown Smoke Indicates Burning Class A Materials
Notes: 26

## Slide 27: “Velvety Smoke” or “Boiling” Movement, Is Smoke That Moves Rapidly Skyward, Is Highly Heated Smoke That Is About To Ignite
Notes: 27

## Slide 28: Black Smoke= Petroleum Products, Foam Rubber, Plastics
Notes: 28

## Slide 29: Today that’s not still true
Notes: 29

## Slide 30
Smoke Location is NOT always Fire Location
Notes: 30

## Slide 31: Any Level With Smoke Must Be Checked Out!
AND The Floor Below !
Notes: 31

## Slide 32: Beware of changing conditions !
Notes: 32

## Slide 33: Have A Safe Haven
Notes: 33

## Slide 34: Don’t Be Caught by Flashover
Notes: 34

## Slide 35: Smoke Conditions May Be Your Last Warning Before Fire “Lights Up” BUT Smoke Can Also Conceal Fire
Notes: 35

## Slide 36: Of The 48 Burn Deaths
15 Caught by Structural Collapse
21 Caught or Trapped by Fire Growth, Flashover, or Backdraft
5 Lost/Disoriented in Structure
5 Fell Through Holes in Floor
2 Struck by Falling Debris
Notes: 36

## Slide 37: Plastic’s Heat Release Rate & Volume
One pound of paper
  7,100 BTU’S
One pound of styrene plastic
  18,000 + BTU’S/lb.
  3,500 x 18,000=63,0000,000 BTUs (AKA a Whole Lot)
Notes: 37

## Slide 38: Heat Release Rates & Volumes
2’ diameter pool of Gasoline 380
Upholstered Cotton Chair 351 70 Lbs
Dry Christmas Tree 474
Uphlst’d Polyurethane Fm Chair 1990 62 lbs
Cotton/Jute Mattress 55 lbs 385
Polyurethane Foam Mattress 2493 32 lbs
BTUs

## Slide 39: This Compresses The Stages of Fire Development
Notes: 39

## Slide 40: Compressed Stages of Fire Development
At the same time, FD is arriving sooner due to improvements in alarm systems, cell phones etc.
Notes: 40

## Slide 41: Impacts of Time
Fire doubles in size each minute*
Flashover occurs in 2 to 3 minutes.
Lightweight truss fails in 4 to 5 minutes.
Steel bar joists fail in 5 minutes.
Our average reflex time is 8-10 minutes.
Notes: 41

## Slide 42: Flame Spread Rates
Some plastics exhibit a flame spread rate of 2 feet per second!!
That is 10 times faster than most wood surfaces

## Slide 43: Flashover- Ignition of Entire Room
Usually gives warnings:
Rising heat levels
Rollover
PPE can delay detection of heat warning signs!!
Notes: 43

## Slide 44: Rollover Is the Ignition of Fuel Gases (Smoke) at Ceiling Level Ahead of the Main Body of Fire. Smoke Can Hide Rollover.
Notes: 44

## Slide 45: Rollover is your last warning before flashover. You must either cool the area, or get out!
Notes: 45

## Slide 46: Flash- over !
Notes: 46

## Slide 47: Firefighters must understand this environment but more importantly, We Must Know How to React
Notes: 47

## Slide 48: There are only 2 choices..1-adequately cool
Notes: 48

## Slide 49: Or 2- GET OUT PPE can only protect you for about 2 seconds after flashover. You must cool the fire or, get out, or else you start burning
Notes: 49

## Slide 50: How about ventilation?
19:35:31
Notes: 50

## Slide 51: Ventilation will NOT prevent flashover
Notes: 51

## Slide 52
Ventilation will hasten flashover in ventilation limited fires
Notes: 52

## Slide 53: No matter what PPE you wear, or what you may have heard, Flashover is NOT a survivable event !
Notes: 53

## Slide 54: Understand the changing environment
Temperature
Time

## Slide 55
Temperature
Time
Understand the changing environment

## Slide 56
Notes: 56

## Slide 57: Reasons for Firefighter Deaths Unpredictable Fire Behavior
BACKDRAFT !
Notes: 57

## Slide 58: What is a Backdraft?
A Backdraft is an instantaneous ignition of Fuel Gases (Smoke) that results in an explosion.
Notes: 58

## Slide 59: What Causes A Backdraft ?
A Backdraft is caused by admitting air into a superheated, oxygen deficient atmosphere that is rich in fuel.
Notes: 59

## Slide 60: What are the warning signs of potential backdraft?
Oxygen Deficient Smoke is Grey-Yellow in Color
Notes: 60

## Slide 61: Backdrafts Can Be Extremely Powerful Explosions !
This one blew down a 12” brick wall burying 3 firefighters
Notes: 61

## Slide 62: Most Backdrafts Occur in the Decay Phase
Notes: 62

## Slide 63: How Do We Prevent A Backdraft?
This Backdraft blew the gate out of it’s track!
Notes: 63

## Slide 64: Vertical Ventilation !
Notes: 64

## Slide 65: What Good Will Vertical Venting Do Here?
Notes: 65

## Slide 66: Every separate space is a different balloon!

## Slide 67: Backdrafts Can Occur in Voids That Are in Proximity to the Fire, Even Where the Fire Is Free Burning

## Slide 68: Building Construction Impacts on Firefighter Survival
Notes: 68

## Slide 69
Q. What do these buildings have in common?
Notes: 69

## Slide 70
A. They’re all the scene of at least one firefighters death where the building played a major role!!
Notes: 70

## Slide 71: Cultivating a 300 year old mind.
Notes: 71

## Slide 72: Make Friends with Brannigan & Dunn

## Slide 73: KNOW the classes of construction and their hazards from fire
Notes: 73

## Slide 74: Which Fires Are Related?
23rd St Fire, NYC 1966 -12 LODD
Vendome Hotel, Boston, 1972, 9 LODD
Waldbaum’s Supermarket, 1978 -6 LODD
Macy’s Dept Store, NYC 1979, 1 LODD
Hackensack Ford, NJ, 1988-5 LODD
Gift Shop, Orange Co Fla, 1989 2 LODD
Brackenridge Pa, 1991 – 4 LODD
Mary Pang Fire, Seattle 1995- 4 LODD
Houston Mc Donald's, 2000-2 LODD
Sofa Store, Charleston SC, 2007 9 LODD

## Slide 75: Which Fires Are Related?
23rd St Fire, NYC 1966 -12 LODD
Vendome Hotel, Boston, 1972, 9 LODD
Waldbaum’s Supermarket, 1978 -6 LODD
Macy’s Dept Store, NYC 1979, 1 LODD
Hackensack Ford, NJ, 1988-5 LODD
Gift Shop, Orange Co Fla, 1989 2 LODD
Brackenridge Pa, 1991 – 4 LODD
Mary Pang Fire, Seattle 1995- 4 LODD
Houston Mc Donald's, 2000-2 LODD
Sofa Store, Charleston SC, 2007 9 LODD

## Slide 76: Building Construction Impacts
Flame Spread and Smoke Production
Notes: 76

## Slide 77: Building Construction Impacts
Exit Travel Distances
Notes: 77

## Slide 78: Building Construction Impacts
Airflow Characteristics-IN
Notes: 78

## Slide 79: Airflow Out- Tight Building Syndrome

## Slide 80: Airflow Characteristics
Notes: 80

## Slide 81: Acetylene –1200 Degrees
Notes: 81

## Slide 82: Oxy-Acetylene – 5,500 Degrees
Notes: 82

## Slide 83: A Closed Door Is the Difference Between Life and Death
Notes: 83

## Slide 84: SOP’s only work at “Standard” Fires
Notes: 84

## Slide 85: Houston, 2009- 2 LODDs 1 Story PD

## Slide 86: Fire Officers must maintain “State of the Art” knowledge, and use appropriate tactics

## Slide 87
Notes: 87

## Slide 88
Building Geometry
Building Construction Impacts

## Slide 89: A Key Difference Between Stores And Residential Fires...
...Ceiling Height !!
6 Ft
9 Ft of FUEL GAS
Notes: 89

## Slide 90: Building Construction Impacts
Building Geometry
Notes: 90

## Slide 91: Building Construction Impacts
Presence of Hidden Voids
Notes: 91

## Slide 92
What Happens When Ceilings Collapse?

## Slide 93
You Must Get The Ceilings Open !

## Slide 94: Building Construction Impacts
Collapse Potential
Notes: 94

## Slide 95: 249 FF Deaths at Structure Fires 2000-2017*
75 Were Caught in Structural Collapses and were asphyxiated (40), burned (18), or crushed (17).
Source:NFPA / USFA
Notes: 95

## Slide 96: Fire Related Causes of Collapse
Notes: 96

## Slide 97: Fire Related Causes of Collapse
Heating of Unprotected Steel
Notes: 97

## Slide 98: Fire Related Causes of Collapse
Failure of Highly Heated Cast Iron
Notes: 98

## Slide 99: Fire Related Causes of Collapse
Fire Damage to Wooden Structural Elements
Notes: 99

## Slide 100: Fire Related Causes of Collapse
Explosions Fuels, Explosives, Backdrafts
Notes: 100

## Slide 101: Fire Related Causes of Collapse
Expansion of Water Absorbent Materials
Notes: 101

## Slide 102: Fire Related Causes of Collapse
Overloading of Floors or Roof
Notes: 102

## Slide 103: Fire Related Causes of Collapse
Cutting or Removing Structural Elements During Overhaul
Notes: 103

## Slide 104: Fire Related Causes of Collapse
High Winds, Old Age
Notes: 104

## Slide 105: Fire Related Causes of Collapse
Faulty Construction
Shoddy Renovations
Notes: 105

## Slide 106: Fire Related Causes of Collapse
Flooding, Stream Impact,
Notes: 106

## Slide 107: Fire Related Causes of Collapse
Vibrations, Impact Loads
Notes: 107

## Slide 108: Indicators of Potential Collapse
Notes: 108

## Slide 109: Indicators of Potential Collapse
Construction
Notes: 109

## Slide 110: At least 14 FF Deaths involved lightweight wood construction
Notes: 110

## Slide 111: Explosions

## Slide 112: Indicators of Potential Collapse
Problem Occupancy
Notes: 112

## Slide 113: Indicators of Potential Collapse
Heavy fire for 20 minutes or more
Accelerants
Notes: 113

## Slide 114: Pay attention to the elapsed time of burn.
Notes: 114

## Slide 115: Multiple Fires
Notes: 115

## Slide 116: Indicators of Potential Collapse
Cracks or Bulges in Walls
Notes: 116

## Slide 117: Indicators of Potential Collapse
Overloaded Floors
Columns or Walls out of Plumb
Notes: 117

## Slide 118: Indicators of Potential Collapse
Not enough runoff
Notes: 118

## Slide 119: Indicators of Potential Collapse
Smoke or Water Through a Wall
Notes: 119

## Slide 120: Indicators of Potential Collapse
Roofs sagging, or abnormally spongy, pulling away from wall
Notes: 120

## Slide 121
Indicators of Potential Collapse
Notes: 121

## Slide 122: Indicators of Potential Collapse
Building Leaning
Notes: 122

## Slide 123: Indicators of Potential Collapse
Obvious Movement, Plaster Sliding Off, Doors Swinging, Windows Breaking, Creaking, Cracking, Groaning Noises
Notes: 123

## Slide 124: Resistance To Collapse
1-Type 1 Fire Resistive
2-Type 4 Heavy Timber
3-Type 3 Ordinary
4-Type 5 Wood Frame
5-Type 2 Non Combustible
Notes: 124

## Slide 125: Class 1 Fire Resistive*
Notes: 125

## Slide 126: Class 1 Heavyweight
Notes: 126

## Slide 127: Class 1 Lightweight
Notes: 127

## Slide 128: What Types of Collapse Are Possible in a Poured Concrete Bldg?
Notes: 128

## Slide 129: Class 4 Heavy Timber
Notes: 129

## Slide 130: Why Are Heavy Timber Buildings Unlikely to Collapse on Firefighters?
Because the tremendous fire drives us out of the building and out of the collapse zone before collapse is likely.
Notes: 130

## Slide 131: What is the Life Hazard Then From Collapse of a Heavy Timber Building?
Personnel Operating In Exposures
Notes: 131

## Slide 132: Class 3- Ordinary (Brick & Wood Joist)
Notes: 132

## Slide 133
Parapet Wall Collapse
Notes: 133

## Slide 134
Brick Weighs 125 Lbs / Cu. Ft.
1 Ft
2 Ft
1 Ft
= 250 Lbs
Notes: 134

## Slide 135
Will Collapse of This Parapet Kill Firemen?
No ! They’re Outside The Collapse Zone !
Notes: 135

## Slide 136: Now This Is Where Guys Die!
Notes: 136

## Slide 137
This Beam is the problem
Notes: 137

## Slide 138
A 100 Ft. Steel Beam Heated 1000 Degrees Expands 9-1/2”
Notes: 138

## Slide 139
The Sidewalk Is Always In The Collapse Zone !
Notes: 139

## Slide 140
How Wide Should The Collapse Zone Be?
Notes: 140

## Slide 141
Collapse Zone Extends The Entire Length Of the Parapet
Notes: 141

## Slide 142: Exterior collapse deaths are preventable. Establish collapse zones.
Notes: 142

## Slide 143: The collapse zone includes buildings and apparatus

## Slide 144: Problems With Steel
Notes: 144

## Slide 145: Steel “Lally Columns” can explode when heated to 800 degrees

## Slide 146: Class 5 - Wood Frame
Notes: 146

## Slide 147: Class 5 needs 2 categories: Legacy & Lightweight

## Slide 148: 20 Minutes is not guaranteed !
You Must Look For Other Indicators !
Notes: 148

## Slide 149: Of the 49 Crushing/Trauma Deaths
18 Caught in Structural Collapse
9 Fell/Jumped from windows
3 Fell on Debris
18 Struck by explosion debris (backdraft) (9 in ’13)
1 Stuck between a moving part and the building
Notes: 149

## Slide 150: Ways To Cut The Fireground Death Toll
Notes: 150
150

## Slide 151: Tactics for the Modern Environment
Provide water flows adequate for plastics heat release rates
Stage at areas that are not going to be overrun by rapidly advancing flame
Understand fire gas dynamics

## Slide 152: Reasons for Firefighter Deaths
Faulty Fireground Decision Making
2011-2016
50 % of structure fire deaths in Stores, Factories, Public Assembly, Storage, & Vacant Buildings
Notes: 152

## Slide 153: Risk A Lot To Save A Lot
Notes: 153

## Slide 154: Risk Little To Save Little
Notes: 154

## Slide 155: Risk Nothing To Save Nothing
Notes: 155

## Slide 156
Firefighter Deaths per 100,000 fires 2011-2016 Source-NFPA
Notes: 156

## Slide 157: Reasons for Firefighter Deaths Faulty Fireground Decision Making
4 Deaths in Vacant Buildings !
Notes: 157

## Slide 158: Vacant Buildings Identified & Hazards Marked
Notes: 158

## Slide 159
Normal stability when marked,
Hazards, Interior Ops only after exam & with extreme caution
Exterior Ops. Enter only after exam, w/ OK of IC for short time, min. staff
Notes: 159

## Slide 160: Take Action On Hazards!!!
Notes: 160

## Slide 161: Reasons for Firefighter Deaths Attitude!
Notes: 161
161

## Slide 162: Firefighter Survival
Rule #1
  Never put yourself in a position where you are depending on someone else to get you out!

## Slide 163: Firefighter Survival
Rule #2
  ALWAYS know where your escape route is.

## Slide 164: Firefighter Survival
Rule #3
  Always know where your second escape route is.

## Slide 165: Give All Firefighters High Quality, Live Fire Training
Notes: 165
165

## Slide 166: Establish Mandatory Minimum Standards for Officer Training
Notes: 166
166

## Slide 167: Provide Adequate Staffing
Too few people slows completion of vital tasks, hoselines are stretched later, ladders don’t get raised on time, ventilation doesn’t get done.
Increases stress on members, 26 Heart Attacks & Strokes in 2016
Notes: 167
167

## Slide 168: It takes people to do this job !!
Notes: 168
168

## Slide 169: Effective Fireground Supervision Promotes Firefighter Safety Through Proper Risk Management
Notes: 169
169

## Slide 170: Forward Deployment Of Chief Officers Puts Them In Position To Make Correct Decisions
Notes: 170

## Slide 171: Employ Safety Officers
Reports Directly To The Incident Commander
Has The Authority To Stop or Modify Dangerous Operations
Shall Monitor Overall Scene Safety & Specific Concerns of IC
Is Not To Get Involved In Tactical Operations
Notes: 171

## Slide 172: Use and Enforce an Accountability System
That means more than just hanging tags on a helmet!!
Notes: 172

## Slide 173: Invest in Your Firefighter’s Safety. The fireground is no place for ‘good enough’
Notes: 173
173

## Slide 174
In spite of our best efforts however, the unexpected, unpredictable event can still happen on the fireground
Notes: 174

## Slide 175: Train & Use Rapid Intervention Teams
Notes: 175
175

## Slide 176: They Have Saved Firefighters Lives!! But They Must Be Properly Staffed, Trained, Equipped, and Motivated
Notes: 176
176

## Slide 177: Solve The Most Life Threatening Problems First !!
FIRE
AIR
Medical
Removal
Notes: 177
177

## Slide 178: Get Them AIR !
Notes: 178

## Slide 179: Bring A RIT PAK or Spare Mask for Each Downed FF
Notes: 179

## Slide 180: Make Thermal Imagers Available At Every Operating Location.
They are especially critical to
Rapid Intervention Teams
Notes: 180
180

## Slide 181: Promote Firefighter Survival Training
Notes: 181

## Slide 182: It’s a Whole Lot Easier to Bailout in a Hurry If Need Be When You Have Done It Before in Practice!
Notes: 182

## Slide 183
Firefighter Survival Techniques
Maintain control of the door to the fire area
Control ventilation
Have a safe haven before committing to above the fire
Notes: 183

## Slide 184: When The Search is Complete, Get to a Safe Area
Notes: 184

## Slide 185: Firefighter Survival Techniques
If cut off by FIRE….
Close doors between you & fire
Call for help, use radio & PASS
Locate ANY exit-
Breach a partition- TOOLS
Emergency window bailout
Notes: 185

## Slide 186: Make sure you always have two ways out.
Notes: 186

## Slide 187: Your Dept can spend thousands to buy you ropes and harnesses, and train you in its use, but it ain’t worth a damn if you don’t carry it and prepare yourself mentally for its use!
Notes: 187

## Slide 188: When Water Problems Occur, Get People To Safe Areas
Notes: 188

## Slide 189: Promote Wellness & Rehab Programs
Enforce Mandatory Fireground Retirement Age of 65
Notes: 189

## Slide 190: Be Alert For Building Alterations And Unusual Conditions
STOP IF SOMETHING DOES’NT FEEL RIGHT!

## Slide 191
Altered Buildings Kill Firefighters!
Steel Plating Adds Weight
Holds Heat, Accelerates Flashover
Delays or Prevents Ventilation
Accelerates Collapse

## Slide 192
Take Action On Hazards ! !

## Slide 193
Get Out and Pre-plan Your Area

## Slide 194
Everyone Can Have A 3 - Ring Binder
G.I./G.O.
Notes: 194

## Slide 195: Learn your buildings, before..
Notes: 195

## Slide 196: …NOT after the fire!
Notes: 196

## Slide 197: Because After the Fire Is Way Too Late!
Notes: 197

## Slide 198
How Do We Motivate Our People To Take Their Responsibility Seriously?
Notes: 198

## Slide 199
If That’s Your Kid In That Box, And You Could Have Prevented It, How Could You Look At Yourself In The Mirror?
Notes: 199

## Slide 200: Bring All Your People Home Safely !
Notes: 200

## Slide 201: And finally, the Number 1 proven way to keep your firefighters from killing themselves in structural fires……

## Slide 202: Advocate, Mandate, and Install automatic sprinklers in every structure…. Including your own homes!!!

## Slide 203: 99 Firefighters committed suicide in 2016! We must support suicide prevention efforts.
Source NFPA and Firefighter Behavioral Health Alliance

## Slide 204: Please pray for our troops
Notes: 204

## Slide 205: Thanks to NIST and UL for their research and continuing efforts to make firefighters safer. ww.nist.gov/fire ww.ul.com/global/eng/pages/ newscience/firesafety
Thanks to NYSPFF and NYSDOL
for sponsoring this opportunity to share with fellow firefighters
Notes: 205

## Slide 206: For comments, copies of this presentation, or further info:
www.chiefnorman.com
Stay Safe. BE Careful!
Notes: 206

## Slide 207: Be CAREFUL ! Stay Safe. Thanks to all the Fire Photographers who share their pictures so that others may learn. R.I.P. Harvey
Notes: 207